## Slide 1: Meteorological conditions of the production environment
Meteorological conditions of the production environment - temperature, relative humidity and speed of air movement determine the intensity of heat exchange between the human body and the environment and have a significant effect on the functional state of various body systems, well-being, performance, productivity, health.
Prolonged exposure to human adverse(неблагоприятый) meteorological factors dramatically worsens the health of the body and can lead to illness.
Meteorological conditions of industrial buildings and premises are subject to fluctuations of a seasonal nature. The meteorological conditions of industrial buildings and premises are greatly influenced by the technological process.
Reduced and increased temperature, humidity and air mobility adversely affect the health and performance of people.

## Slide 2
The effect of high temperature on a person contributes to the rapid fatigue(утомляемость) of the worker, can lead in certain conditions to an overheating of the body, accompanied by an increase in body temperature, excessive sweating(потоотделение), thirst, rapid breathing and pulse. With a more significant overheating of the human body, dizziness(головокружение) also rises, speech is difficult, etc. The described form of body overheating with a predominance of a sharp increase in body temperature is called thermal hyperthermia.

## Slide 3
Another form of heat exposure per person is characterized by a disturbance of water-salt metabolism and is known as the convulsive(судорожная) disease. It takes the form of cramps(судорога) of various muscles, especially the calf(икраножная), accompanied by a large release of sweat(пот) with the loss of the body's desired salts. Dehydration of the body causes thickening(сгущение) of the blood, the nutrition of tissues and organs worsens. The loss of salts deprives the blood of the ability to retain water, which leads to the rapid removal of the newly drunk fluid from the body.

## Slide 4
Subsequently thermal shock may come a heat stroke(тепловой удар), flowing with loss of consciousness(сознание), increase in body temperature to 40 - 41 ° C, weak and rapid pulse. With a warm or sunny impact, blood rushes to the brain, causing the victim to feel a sudden weakness, a headache, vomiting, and breathing becomes superficial. A characteristic sign of severe damage is almost complete cessation of sweating. Heat stroke and convulsive illness can lead to death.

## Slide 5
An adverse effect on the human body has also a low air temperature. It can cause local or general cooling of the body, cause a cold or frostbite. Prolonged cooling often leads to a breakdown in the activity of capillaries and small arteries (fever of fingers, toes and tips of the ears). At the same time, there is a hypothermia(переохлаждение) of the whole organism.

## Slide 6
These parameters both separately and in a complex have a significant effect on the course of life processes in the human body, largely determine its health and therefore are an important characteristic of hygienic working conditions.
Unfavorable weather conditions can lead to rapid fatigue(утомлемость), increased morbidity and reduced productivity.
Thus, air temperature can significantly affect the thermoregulation of the body, which is due to biochemical and biophysical processes, which causes a constant heat exchange of the organism with the external environment.

## Slide 7
Thermoregulation is a combination of physiological processes aimed at maintaining the relative constancy of body temperature in conditions of changing the temperature of the environment. Thermoregulation is aimed at preventing violations of the heat balance of the body or its restoration.
It is generally accepted that thermoregulation is inherent only in homeothermic animals (including mammals (including humans) and birds), whose bodies have the ability to maintain the temperature of the internal areas of the body at a relatively constant and fairly high level (about 37-38 ° C in mammals And 40-42 ° C in birds) regardless of changes in ambient temperature.
Thermoreceptors transmit information about the thermal state of the body to the thermoregulatory centers, in turn, the centers of thermoregulation through nerve fibers, hormones and other biologically active substances change the level of heat transfer and heat production of the body.

## Slide 8
Thermoregulation can be divided into two main types:
1. Physical thermoregulation:
- Evaporation (sweating);
- Radiation (radiation);
- Thermal conduct (conduction);
- Convection.
2. Chemical thermoregulation.
- Contractive thermogenesis;
- Unconclusive thermogenesis.

## Slide 9
Physical thermoregulation is carried out due to changes in the activity of the cardiovascular system (expansion of blood vessels and increased blood flow to the skin) and the work of muscle tissues.
Physical thermoregulation ensures the preservation of the constant temperature of the body due to changes in the heat output of the body by carrying through the skin (conduction and convection), radiation and evaporation of water.
A person at rest at an air temperature of about 20 ° C and the total heat transfer, equal to 419 kJ (100 kcal) per hour, using 66% of the radiation is lost, the evaporation of water - 19%, convection - 15% of total body heat loss.

## Slide 10
Chemical thermoregulation (the process that provides the formation of heat in the body) is due to a change in the intensity of processes in the metabolism and oxidative processes. It is realized through the metabolism and through the heat production of such tissues as muscles, as well as the liver, brown fat, that is, by changing the level of heat formation - by increasing or weakening the intensity of metabolism in the cells of the body. When oxidizing organic substances, energy is released.
An increase in the temperature of the surrounding environment causes a reflex decrease in the metabolism, and as a result, heat production in the body decreases. With a decrease in the ambient temperature, the intensity of metabolic processes increases reflexively and heat formation increases.

## Slide 11
Evaporation (sweating) is the release of heat energy into the environment due to the evaporation of perspiration or moisture from the surface of the skin and mucous membranes of the respiratory tract.
Evaporation is divided into 2 types:
A) Unperceptible perspiration (without the participation of sweat glands) is the evaporation of water from the surface of the lungs, mucous membranes of the respiratory tract and water seeping through the epithelium of the skin (evaporation from the skin surface is even if the skin is dry).
B) Sensible perspiration (with the active participation of sweat glands) is the return of heat by the evaporation of perspiration. On average, 400-500 ml of sweat is allocated per day at a comfortable temperature of the medium, hence, up to 300 kcal of energy is given. Evaporation of 1 l of sweat in a person with a body weight of 75 kg can lower body temperature by 10 ° C.
At 100% humidity, evaporation is not possible. At high humidity of atmospheric air the high temperature is transferred more heavily, than at low humidity.

## Slide 12
Radiation is a way of delivering heat to the environment by the surface of the human body in the form of electromagnetic waves of the infrared range (a = 5-20 microns). At the expense of radiation energy is given to all objects, the temperature of which is higher than absolute zero. Electromagnetic radiation freely passes through the vacuum, atmospheric air for it, too, can be considered "transparent."
As you know, any object that is heated above the ambient temperature, emits heat.

## Slide 13
Thermal conductance (conduction) is a method of heat release, which takes place during contact, contact of the human body with other physical bodies. The amount of heat released by the body to the environment in this way is proportional to the difference in the average temperatures of the contacting bodies, the area of the contacting surfaces, the time of thermal contact, and the thermal conductivity of the contacting body.

## Slide 14
Convection is a method of heat transfer of an organism, carried out by the transfer of heat by moving particles of air (water). In conditions where the air temperature is 20 ° C and the relative humidity is 40-60%, the adult body dissipates about 25-30% of the heat to the environment through thermal conductivity and convection. The essence of the convection process lies in the following: our body heats the air near the skin; The heated air becomes lighter than the cold air and rises, and it is replaced by cold air, which again heats up. In fact, we are warmed not by clothes, but by the air that it holds.

## Slide 15: Normalization of meteorological conditions of the production environment
The basis for the normalization of the meteorological conditions of the production environment is the assessment of meteorological conditions as optimal and permissible depending on the category of work in terms of severity, time of year, and thermal characteristics of the production facility.
Depending on the amount of energy consumption, all work is divided into categories of gravity, and the permissible values of the intensity of thermal irradiation from production sources are established, depending on the percentage of the irradiated surface of the body of workers.

## Slide 16
Basic normative documents: GOST 12.1.005 SSBT "General sanitary and hygienic requirements for the air of the sanitary zone"; SanPiN 9-80 RB 98 "Hygienic requirements for the microclimate of industrial premises".
Indicators characterizing the microclimate are:
1) air temperature;
2) relative humidity of air;
3) the speed of air movement;
4) the intensity of thermal radiation.

## Slide 17: Creation of optimal meteorological conditions of labor in industrial premises is carried out in the following directions:
Rational volume-planning and constructive solutions of production buildings;
Rational arrangement of equipment;
Mechanization and automation of production processes;
Remote control(дистанционое управление) and surveillance;
Introduction of rational technological processes and equipment;
Rational thermal insulation of equipment;
Protection of people working with different kinds of screens and veils;
Rational ventilation and heating;
Rationalization of the regimes of work and rest;
Use of personal protective equipment.

## Slide 18
Meteorological conditions of work in production (microclimate) are determined by:
Air temperature in the room (t, ° С),
Relative air humidity (φ,%),
Speed of air movement (V, m / s),
Intensity of thermal radiation (P, W / m2).
Meteoconditions - optimal and acceptable in the work zone - regulated depending on the time of year, the category of works on energy consumption and excess sensible heat.

## Slide 19
Optimal microclimatic conditions - a combination of microclimate parameters, which, with prolonged and systematic exposure to humans, ensure the preservation of the normal thermal state of the organism. They provide a sense of thermal comfort and create the prerequisites for a high level of efficiency.
Admissible microclimatic conditions - a combination of microclimate parameters, which, if prolonged and systematically influenced by humans, can cause a change in the body's thermal state that quickly returns to normal. There may be uncomfortable sensations, deterioration of well-being and a decrease in efficiency.
The permissible values of the microclimate indicators are established in cases when optimal standards are not provided for technological requirements, technical and economic reasons.

## Slide 20
Depending on the energy consumption per unit of time, the work is divided into the following categories:
Light physical work (category I) - activities with an energy intensity of up to 174 Watts.
Category Ia includes work done sitting and accompanied by a slight physical strain with an energy consumption of up to 139 W.
The category Ib includes work done sitting, standing or associated with walking and accompanied by some physical stress with an energy expenditure of 140 - 174 W.
Physical works of medium gravity (category II) - activities with an energy intensity of 175 - 290 W.

## Slide 21
Category IIa includes work associated with constant walking, the movement of small (up to 1 kg) items or objects in a standing or sitting position and requiring a certain physical stress with an energy cost of 175 - 232 W.
The category IIb includes work related to walking, moving and carrying weights up to 10 kg and accompanied by moderate physical stress with an energy consumption of 233 - 290 W.
Heavy physical work (category III) - activities with an intensity of energy consumption with an energy consumption of more than 290 watts. These works are associated with constant movement, movement and carrying of significant (over 10 kg) weights and requiring great physical effort.

## Slide 22
Normalizing distinguish two year period: cold (with average outdoor temperature +10 ° C and below) and warm (with average outdoor temperature above +10 ° C).

## Slide 24
Thermoregulation system and human body responses, both physiological (i.e. skin and core temperature) and psychological (thermal sensation and thermal comfort), have been of considerable interest to researchers. However, while reactions to extreme conditions are well understood and explained, there is a considerable knowledge gap for mild temperature range adaptation.
Previous research focused on the whole body response, while local analysis is more appropriate for a new generation of intelligent thermal control systems such as needed in planes. Furthermore majority of previous studies were carried out predominantly on mannequins or with subjects placed in highly
controlled lab chambers, hence adaptations in normal shared spaces is not investigated in sufficient depth. In addition, no study investigated infants’ temperature adaptation.

## Slide 25
Thermoregulation is the mechanism by which the core body temperature of homoeothermic animals is maintained within fairly narrow limits. Thermoregulation occurs as a result of physiological, morphological, and behavioural responses to the environmental conditions. The most important aspects of the environmental conditions
are air temperature, radiant temperatures (infrared and solar radiation), air velocity, humidity, wetting by precipitation or otherwise, and the nature of the floor if insulation is poor [Ingram, 1975]. Thermoregulation is achieved by having control over both heat
production and insulation.
Thermoregulation maintains body temperature stable despite the fluctuations in the environmental conditions, although the peripheral tissue temperatures vary considerably.