## Slide 1
I. Dangerous chemical substances
The classification of dangerous substances is based largely on the
characteristic properties of such substances and their effects on
man.
Legislation on this subject also requires the provision of a
specific pictorial symbol on any container or package.
The following terms are used in the classification of dangerous
substances in the classification, packing and labeling of dangerous
substances regulations .
A. Corrosion
B. Oxidizing
C. Harmful
D. Very toxic and toxic
E. Irritant (раздражающий)
F. Highly flammable (огнеопасный)
G. Explosive

## Slide 2
A. Corrosive
Hazard: Living tissues (живые ткани) as well as equipment are destroyed on contact with these chemicals.
Caution (меры предосторожности): Do not breathe vapors and avoid contact with skin eyes and clothing
B. Oxidizing
Hazard: ignite combustible material (воспламеняющий горючий матреиал) or worsen existing fire and thus make fire fighting more difficult.
Caution: Keep away from combustible material. Restrict smoking in that area.

## Slide 3
C. Harmful
Hazard: Inhalation and insertion of or skin penetration by these
substances is harmful to heath. ( При вдыхании и проникновении через кожу вещества вредны для здоровья)
Caution: Avoid contact with the human body, including inhalation
of vapors and in cases of malaise (недомогание) consult doctor.
D. Very toxic and toxic
Hazard: The substances are very hazardous to health whether
breathed, swallowed (глотать) or in contact with the skin and may
even lead to death.
Caution: Avoid contact with human body, and immediately
consult a doctor in case of malaise.

## Slide 4
E. Irritant
Hazard: May have an irritant effect on skin, eyes and respiratory
organs
Caution: Do not breathe vapors and avoid contact with skin and
Eye
F. Highly Flammable
Hazard: Substances with flash point less than 60 0 C or 140 0F
Caution: keep away source of ignition.
G. Explosive
Hazard: Substances which may explode under certain condition
Caution: Avoid shock, friction, sparks and heat. (удар, трение, искры и тепло)

## Slide 5
Chemical Hazards Evaluation
• Toxicity assessment
• Work activity/risk assessment evaluation
• Assessment of controls effectiveness to block routes of entry (блокировки маршрутов входа)
• Exposure monitoring
• Recommendations for improvement
Chemical Hazards: - Exposure Monitoring
Special instruments - infrared absorption, photoionization, (инфракрасное поглощение, фотоионизация)
gas
Chromatography
Detector tubes
Air sampling and lab analysis
Professional judgment

## Slide 6
Chemical Hazards: Engineering Controls
Substitution (ЗАМЕНА) (use lower toxicity materials)
Enclose processes and otherwise engineer for low emission / low risk
Provide local exhaust to remove airborne agents
Local exhaust ventilation
Need to have even air flow for hoods (ДЛЯ ВЫТЯЖЕК)
Need sufficient make up air
Use Ventilation Manual (руководство) for design
Reduce exposure time
Better procedures
Training
PPE - gloves, face shields, respirators
Remote Operation

## Slide 7
Toxicology is the study of harmful interactions between chemicals
and biological systems.
Man, the other animals and plants in the modern world are increasingly being exposed to chemicals to enormous variety. These chemicals range from metals and inorganic chemicals to large complex organic molecules, yet they are all potentially toxic.
There are now many thousands of chemical substances used in
industry ranging from metals and inorganic compounds to complex
organic chemicals. The people who work in the industries which use
them are therefore at risk of exposure. Fortunately, exposure is often
minimized by using chemicals in closed system so that operators do
not come into contact with them, but this is not always the case. In
third world countries, however, some of which are rapidly
industrializing, exposure levels are higher and industrial diseases
are more common than in the fully developed countries.

## Slide 8
Consequently (как следствие) exposure to toxic substances in the workplace is still a
very real hazard. Furthermore even in the best regulated industrial
environment, accidents may happen and can lead to excessive
exposure to chemicals.

## Slide 9
Industrial diseases have existed ever since man began
manufacturing on a large scale, and during the industrial revolution
occupational disease became common. These diseases were, and some still are of great importance socially, economically and medically. Many occupations carry with them the risk of a particular disease or group of disease.
A man spends on average one-third of his life at work
and, therefore, the environment in that workplace can be a major
factor in determining his health. Although the working environment
has improved immeasurably over the last century, some occupations
are still hazardous despite legislation and efforts to improve
conditions.

## Slide 10: Routes of Entry into the Body
There are main routes by which hazardous chemicals enter the body:
1. Inhalation. For industrial exposure, a major, if not predominant route of entry is inhalation. Any airborne substance can be inhaled. The total amount of a toxic compound absorbed via the respiratory pathways depends on its concentration in the air, the duration of exposure, and the pulmonary ventilation volumes, which increase with higher work loads.
2. Skin Absorption. An important route of entry for some chemicals is absorption through skin. Contact of a substance with skin results in these four possible actions.
- The skin can act as an effective barrier
- The substance can react with the skin and cause local irritation or tissue destruction
- The substance can produce skin sensitization(сенсибилизация)
- The substance can penetrate skin to reach the blood vessels under the skin and enter the bloodstream (Вещество может проникать в кожу, чтобы достичь кровеносных сосудов под кожей и войти в кровоток)

## Slide 11
a. Ingestion (При попадании внутрь). The problem of ingesting chemicals is not widespread in the industry; most workers do not deliberately swallow materials they handle. Nevertheless ,workers can ingest toxic materials as result of eating in contaminated work areas; contaminated fingers and hands can lead to accidental oral intake when a worker eats or smokes on the job
b. Injection (иньекции). Although infrequent in industry, a substance can be injected into some part of the body. This can be done directly into the bloodstream, peritoneal cavity, pleural cavity, skin, muscle, or any other place needle (непосредственно в кровоток, брюшную полость, плевральную полость, кожу, мышцу или любое другое место иглы) or high-pressure orifice (отверстие) can reach

## Slide 12
Dose
The dose is the actual amount of a chemical that enters the body.
The dose received may be due to either acute (short) (острое) or chronic (long-term) exposure. An acute exposure occurs over a very short period of time, usually 24 hours.
Chronic exposures occur over long periods of time such as weeks, months, or years. The amount of
exposure and the type of toxin will determine the toxic effect.

## Slide 13
What is dose-response?
Dose-response is a relationship between exposure and health effect that can be established by measuring the response relative to an increasing dose. This relationship is important in determining the toxicity of a particular substance. It relies on the concept that a dose, or a time of exposure (to a chemical, drug, or toxic substance), will cause an effect (response) on the exposed organism.
Usually, the larger or more intense the dose, the greater the response, or the effect. This is the meaning behind the statement "the dose makes
the poison (яд)."

## Slide 14
Individual susceptibility (восприимчивость)
This term describes the differences in types of responses to hazardous substances, between people. Each person is unique, and because of that, there may be great differences in the response to exposure.
Exposure in one person may have no effect, while a second person may become seriously ill, and a third may develop cancer.

## Slide 15
Sensitive sub-population (чувствительная группа людей)
A sensitive sub-population describes those persons who are more at risk from illness due to exposure to hazardous substances than the average, healthy person.
These persons usually include the very young, the chronically ill, and the very old. It may also include
pregnant women and women of childbearing age. Depending on the type of contaminant (загрязнителя), other factors (e.g., age, weight, lifestyle, sex) could be used to describe the population.

## Slide 16
Deﬁnition and purpose of prevention and toxicovigilance
Prevention is deﬁned as the promotion of health by the individual and the community, and includes identifying departures from good health and intervening to correct them or to minimize their effects.
Prevention of toxic exposures is concerned with preventing chemicals of synthetic or natural origin from reaching people in amounts or at rates that exceed human tolerance to them. It includes identifying and evaluating the causes of poisonings, making predictions about their frequency, and putting into practice measures intended to mitigate or eliminate future exposures or to reduce the severity of health effects after an exposure.
Prevention of exposure is part of the dynamic process of toxicovigilance, which includes identiﬁcation and evaluation of toxic risks and phenomena, and communication with the authorities in order to plan and take action.

## Slide 17
Types of prevention
A toxic exposure occurs when a susceptible individual or population comes into contact with a chemical in a particular environment. The individual may be poisoned as a result. Throughout these guidelines, the term “poisoning” should be understood to include all toxic exposures, including “suspected poisonings” and those that may not result in poisoning. Prevention activities may intervene before, during, or after a “poisoning” event.
Primary poisons prevention activities intervene before the event, aiming to prevent it happening, either by controlling the victim’s access to the agent, controlling the action of an agent upon the victim, or controlling or changing hostile environmental factors. Primary prevention strategies may be active or passive.
• Active strategies seek to change attitudes, lifestyles and behaviours of individuals and groups, for example, by educating communities and individuals about poison awareness and safety practices, or campaigning for initiatives such as safer packaging, labelling and storage of chemical products.
• Passive strategies automatically protect people, by improving the safety of products and the environment where they are used. Once these changes are made, they require little individual effort from the beneﬁciary and can have a far-reaching impact. The best example is given by the childresistant packaging of pharmaceuticals, which has reduced poisoning in children (Rodgers, 1996). Although the safety of reclosable child-resistant closures (CRCs) is only maintained if the user remembers to re-close the container correctly, non-reclosable packaging provides protection without any cooperation from the user. The addition of bittering agents to dangerous liquids, such as ethylene glycol, is another passive strategy to prevent poisoning.

## Slide 18
Education aimed at individuals or communities Prevention of poisoning and chemical safety should be something people learn throughout life in school, home, work and community settings.
Education should aim to:
• raise awareness
• increase knowledge
• change attitudes and behaviour.
Education should seek to persuade people to adopt a “poison prevention” oriented lifestyle by providing them with information and understanding of prevention issues so that they can make their own well-informed decisions, and act on them, assuming responsibility for their own health. Rather than presenting a list of facts with “dos” and “don’ts”, the modern approach to education is to help people to explore their values and attitudes, to see the possible options, then make choices and take action.

## Slide 19
Prevention of toxic substance exposure in the workplace
Modern industries, from small family businesses to large corporations, use chemicals in increasingly diverse workplace environments. There are many tens of thousands of industrial chemicals, many of which can cause health problems as a result of occupational exposure. Effects range from chronic skin diseases caused by solvents to reproductive and developmental problems caused by toxic metals. Health problems due to exposure to toxic substances cause needless human suffering and increase the cost of business. The development of programmes to prevent exposure is an increasingly urgent necessity. It is sound business practice to incorporate prevention principles into business plans and goals, and thereby reduce absence due to ill health, medical costs and insurance rates.

## Slide 20
1. Planning prevention and deﬁning responsibility Development of a prevention programme requires commitment of resources and an internal structure that deﬁnes who is responsible, what they are responsible for, and how the programme is going to be implemented. All people involved in the process must value the concept of prevention. If the business is large enough, a toxic substance committee could be formed to provide structure and focus the prevention effort. The committee may be composed of safety managers, manufacturing supervisors, purchasing agents, warehouse personnel, engineers, and research and development personnel. The monthly committee duties may involve reviewing new chemicals purchased by the company to decide where they can be stored, which employees need to be trained in handling and use, and what kind of personal protective clothing is needed.

## Slide 21
2. Deﬁning the scope of the programme The scope of the programme needs to be clearly deﬁned, in terms of the chemicals and products to be included in the programme and the employees who may be exposed to them. This initial deﬁnition focuses the programme and ensures it is comprehensive.
3. Prevention of toxic substance exposure in the workplace
4. Raising awareness
Employees must be made aware of the existence of the programme by means of awareness campaigns with posters, active training and participatory events. This will give employees ownership of the programme and empower them.
5. Risk characterization
The risk associated with each substance must be weighted in relation to other substances and workplace hazards.

## Slide 22: II.Harmful substances and poisoning prevention Harmful substances and their classification. The effect of harmful substances on the human body. Rationing of harmful substances in the air of the working area and determination methods. Methods for the prevention of occupational poisoning and disease. - 2 hours

## Slide 23
Harmful substance - a substance which, in contact with the human body in case of violation of safety requirements, can cause work-related injuries, occupational diseases or deviations in the state of health, detected by modern methods, both during work and in the long-term life of the present and subsequent generations.

## Slide 24
By the nature of the effect on the human body, six groups of substances are distinguished:
toxic,
irritating,
sensitizing,
carcinogenic,
mutagenic, affecting reproductive function (SSBT. Dangerous and harmful production factors. Classification ").
1. Toxic chemicals have a harmful effect on the human body, cause disorders of the nervous system, muscle cramps, affect the blood-forming organs, interact with blood hemoglobin.

## Slide 25
Irritating harmful substances are substances that cause irritation of the mucous membranes (слизистой оболочки) of the respiratory tract, eyes, lungs, skin integuments, cause changes in their state or activity in living objects.
Sensitizing substances - substances that cause increased sensitivity and violent reactions during subsequent contacts, most often leading to skin changes, asthmatic phenomena, blood diseases, and decreased immunity.
Carcinogenic substances (Greek: "giving birth to cancer") (blastomogenic) - substances cause the development of malignant tumors.

## Slide 26
Mutagenic substances affect the genetic apparatus of germinal and somatic cells of the body. This can cause a decrease in the body's overall resistance, early aging, and in some cases serious diseases. The effect of mutagenic substances can affect the offspring (not always of the first, and possibly second and third generations).
Substances affecting the reproductive function (reproduction of offspring) of a person cause the occurrence of congenital malformations and deviations from normal development in offspring, affect the intrauterine and postnatal development of offspring.

## Slide 27
By the degree of exposure to the body, harmful substances are divided into four hazard classes (On approval of the technical regulation "Safety requirements for toxic and highly toxic substances» Decree of the Government of the Republic of Kazakhstan dated November 19, 2010 No. 1219):
- 1st class - substances are extremely dangerous;
- 2nd class - highly hazardous substances;
- 3rd class - moderately hazardous substances;
- 4th class - low-hazard substances.

## Slide 28
The hazard class of harmful substances is established depending on indicators and their norms characterizing the effect of the effects of poisons on the body along the pathways of their penetration

## Slide 29
Factors to be avoided in hazardous production processes regarding the likelihood of harm to human health, living organism and the environment are:
1) the risk of toxic and highly toxic effects on humans and living organisms by inhalation (inhalation exposure) of toxic chemical products;
2) the risk of toxic effects of hazardous products that cause visible necrosis (damage) of the skin of the human body and living organism;
3) the risk of toxic effects of hazardous products causing irreversible effects in contact with eyes;
4) the risk of toxic effects of hazardous products on the human body with a sensitizing effect by inhalation, which is expressed as an increased sensitivity reaction (asthma, rhinitis, conjunctivitis, alveolitis);
5) the risk of toxic effects of hazardous products on the human body, which has a sensitizing effect in contact with skin, which can lead to allergic contact dermatitis;
6) the risk of toxic effects of hazardous products on the human body and living organism, causing mutations in somatic cells;
7) the risk of toxic effects of hazardous products on the human body and living organism, causing carcinogenicity to humans and living organisms;
8) the risk of toxic effects of hazardous products on the human body and living organism, which has a harmful effect on the reproduction function;
9) the risk of toxic effects of hazardous products on the human body and a living organism, having a harmful effect on the target organ and / or system in the human or animal body with a single and chronic exposure;
10) the risk of the harmful effects of hazardous products with acute toxicity in the aquatic environment on fish and other aquatic animals, algae, which can lead to significant toxic effects on them;
11) the risk of the harmful effects of hazardous products with chronic aquatic toxicity on fish and other aquatic animals, algae, which can lead to significant toxic effects on them;
12) the risk of surface water pollution of water bodies of drinking and cultural and domestic water use;
13) the risk of contamination with hazardous products of atmospheric air;
14) the risk of contamination with hazardous soil products;
15) harmful effects on the environment of hazardous industrial wastes;
16) the risk of contamination of food products with heavy metals and arsenic, nitrosamines, benzo (a) prins, polychlorinated biphenyls and histamines at all stages of agricultural and industrial production of food raw materials and food products, as well as their storage, packaging and labeling;
17) the risk of the harmful effects of industrial waste on the environment.

## Slide 30
This Technical Regulation uses the concepts provided for by the laws of the Republic of Kazakhstan dated November 9, 2004 "On Technical Regulation" and dated April 3, 2002 "On Industrial Safety at Hazardous Production Facilities", as well as the following:
1) dose - the amount of a substance that has been ingested or introduced into the body, or a long-term exposure of an organism to a factor, taking into account its intensity;
2) lethal dose - the minimum amount of a harmful substance or exposure, the ingestion or exposure of which on the body leads to the death of the latter;
3) toxic dose - the minimum amount of a toxic substance that leads to poisoning of the body;
4) hazardous products - hazardous chemical products, hazardous food products, hazardous waste, which includes at least one toxic substance that affects human health and the environment,
5) warning labeling - information on the hazardous properties of hazardous products and on safety measures at the stages of handling it, applied to products and (or) packaging in accordance with the requirements of technical regulations in the field of safety of products containing toxic and highly toxic substances;
6) product safety data sheet - a document containing information on the characteristics of hazardous products and measures to ensure safe handling of them;
7) chemical products - products that have passed the technological stages of separation from natural resources and (or) transformation of raw materials using chemical reactions and are suitable for use on the day of meeting human needs or for production in the form in which it was released by the manufacturer;
8) hazardous chemical products - chemicals with properties that can have a harmful effect on human life and health, the environment;
9) classification of hazardous chemical products - the division of chemical products containing toxic and highly toxic substances into hazard classes and categories of chemicals to identify its properties that have or may have a harmful effect on human life and health, the environment;

## Slide 31
10) maximum permissible concentration (hereinafter - MPC) - the maximum amount of a harmful chemical substance per unit volume, which, if daily exposed for a long time, does not have a harmful effect on the human body, as detected by modern research methods; It is a genetic criterion in assessing the sanitary-epidemiological state of the environment (air of the working zone, atmospheric air, water bodies and soil);
11) approximate permissible levels (hereinafter - ODE) - permissible levels of substances in the water, developed on the basis of calculated and express experimental methods for predicting toxicity and applicable only at the stage of preventive sanitary supervision of designed or constructed enterprises, treatment facilities;
12) circulation of hazardous products - the implementation of production, processing, acquisition, storage, sale, use and destruction of hazardous products on the territory of the Republic of Kazakhstan.

## Slide 32
Warning labeling of hazardous products must indicate that more complete information on the safe handling of hazardous products is in the safety data sheet.
Marking in the territory of the Republic of Kazakhstan should be made in the Kazakh and Russian languages; additional use of foreign languages ​​is allowed.
Warning labels should be distinguished from other information accompanying hazardous products. Warning labels must be clear and legible, resistant to chemicals, climatic factors, stored throughout the entire period of storage and use of hazardous products.

## Slide 33
The safety data sheet must contain the following sections:
1) identification of hazardous products and information about the manufacturer or supplier;
2) hazard identification (s);
3) toxicity information;
4) First aid measures;
5)measures to prevent and eliminate emergency and emergency situations and their consequences;
6) rules for storing hazardous products and handling them during loading and unloading;
7) hazardous exposure controls and personal protective equipment;
8) physicochemical properties;
9) stability and reactivity;
10) information on the environmental impact;
11) recommendations for the disposal of toxic waste;
12) information during transportation. (The procedure for packaging and labeling hazardous waste for transportation purposes is established by the legislation of the Republic of Kazakhstan on transport);
13) information on national and international legislation;
14) additional information or a document certifying the safety of food products.

## Slide 34: Requirements for hazardous industrial processes
In the production of hazardous products, standards must be established that ensure safety for the life and health of production personnel, environmental protection in accordance with the requirements of the labor legislation of the Republic of Kazakhstan.
Personnel engaged in the stages of the life cycle of hazardous products must have the necessary qualifications, knowledge of safe working methods, be provided with the necessary means of control and protection, and have appropriate approvals for working with hazardous products in the manner established by the legislation of the Republic of Kazakhstan.
In order to ensure the safety of personnel employed at all stages of the life cycle of hazardous products, the conditions must be met:
1) the use of techniques and methods of labor protection, eliminating the risk of exposure to hazardous products on human life and health, the environment;
2) the provision of necessary personal hygiene products, personal protective equipment;
3) the use of warning labels;
4) familiarization of personnel with measures of safe work with chemical products;
5) development of measures for the prevention and elimination of emergency situations;
6) development of organization standards for working personnel on general requirements when working with toxic and highly toxic substances and safety and labor protection instructions, including requirements for work in closed apparatus, wells, collectors and other similar equipment, tanks and structures at enterprises production of hazardous products.

## Slide 35
At industrial facilities, the production activity of which is associated with toxic and highly toxic substances, should be:
1) normative documents on standardization of labor safety during the production (manufacture), use and storage of toxic and highly toxic substances have been developed;
2) complexes of organizational and technical, sanitary-epidemiological and biomedical measures were completed.
The limit quantities of toxic and highly toxic substances, the presence of which at the industrial facility is the basis for declaration, are established in the Law of the Republic of Kazakhstan "On Industrial Safety at Hazardous Production Facilities".

## Slide 36
Monitoring of the air environment of industrial premises is carried out according to a schedule approved by the chief engineer of the enterprise.
Air sampling is carried out in the working area at a distance of 0.5 m from sources of harmful substances in the conditions of the existing supply and exhaust ventilation outside the action of the supply ventilation torch and open windows.
Typically, the frequency of sampling and analysis is set depending on the hazard class of substances: 1st hazard class - at least once every 10 days, 2nd - at least once a month, 3rd and 4th hazard classes - not less than once a quarter.
To control the air environment, laboratory, indicator and express methods are used. There are also automatic gas monitoring devices.

## Slide 37
Laboratory methods are very accurate and make it possible to determine the trace amounts of toxic substances in the air. In this case, an air sample is taken in the production room, and analyzed in the laboratory. However, they require considerable time and are mainly used in research. For this purpose, various methods of chemical (bulk and weight) and physicochemical (photocolorimetry, spectroscopy, coulometry, chromatography, polarography, etc.) analysis are used.
Indication methods are simple, they allow you to quickly determine the qualitative composition of pollutants. These methods are used in cases where the presence of toxic substances in the premises is undesirable even in low concentrations, and if they are available, special urgent measures are required (start-up of emergency ventilation, neutralization of the gas-polluted area, use of personal protective equipment, etc.). However, the quantitative determination of toxic substances in air using indicator methods can be made very tentatively.
Indication methods are based on color reactions between polluted air and an absorption solution or reactive paper. By the intensity of the color of the absorber, we can tentatively judge the concentration of the analyte in the air. So, a piece of paper saturated with lead acetic acid blackens in the presence of traces of hydrogen sulfide; a piece of paper soaked in dimethylaminobenzenedehyde vapor (Prokofiev's piece of paper) turns red in the presence of traces of phosgene, etc.

## Slide 38
Express methods are used for qualitative and quantitative determination of the concentration of harmful vapors and gases directly in the working area. For monitoring, gas analyzers of the UG brands, a chemical gas detector GC, a gas analyzer of the type PGF 2M1-IZG, etc. are used.
Express methods are mainly based on obtaining a color reaction in the interaction of the analyte with a solid sorbent - indicator powder, placed in a narrow glass tube. When contaminated air is sucked through the tube, the indicator powder is painted for a certain length, the value of which determines the concentration of the analyte. The main principles of the linear coloristic method are implemented in gas analyzers UG-1 and UG-2.

## Slide 39
Continuous automatic gas analyzers usually carry out continuous recording of the level of gas contamination on a chart tape. They may have varying sensitivities. Gas analyzers tuned to MPC levels or explosive hazard indicators ™, when they reach the appropriate concentration, give a light or sound signal, automatically turn on ventilation, etc. Such devices are called gas detectors.
To determine the concentration of dust in the air, there are several methods:
1. aspiration - based on air suction through porous materials or through liquids (water, oils). However, standard filters are most often used. Filters AFA-VP-20, AFA-KhP-20, AFA-HA-20, AFA-VP-10, FPP made of various polymeric filtering materials are found to be most widely used;
2. sedimentation - based on the natural deposition of dust on glass plates with the subsequent calculation of the mass of dust per 1 m2 of surface;
3. electrostatic - consists in creating a high voltage field in which dust particles are electrified and attracted to the electrodes;
4. photometric - dust particles are recorded using strong side light;
5. radioisotope - based on determining the mass of dust retained by the filter by the degree of attenuation of the flux of P particles passing through the filter before it is dusted and after.

## Slide 40: The combined effect of chemical substances
There are three possible effects (Fig.) Of combined exposure:

## Slide 41
1 - summation (additivity) - the phenomenon of summing up the effects induced by the combined action;
2 - potentiation (synergism) - strengthening the effect of the effect (effect in excess of the summation);
3 - antagonism - the effect of the combined effect is less than expected during summation, when exposed to substances in a mixture, one substance weakens the effect of another, and the effect is less than with summation. The use of antidotes is based on the effect of antagonism (For example, nalorphine is the antagonist (antidote) of morphine);
4 - the independent action of toxic substances in the mixture has a combined effect that does not differ from the isolated action of each poison separately. (For example, a mixture of car exhaust and road dust has an independent effect). The effect of the most toxic substance may prevail.